## Slide 1
Embedded Systems Project : AXI4-lite Prof. W. Fornaciari Prof. D. Zoni Tutor: Andrea Galimberti
Group
Colombi Marco
Corbetta Giorgio
Consonni Cesare

## Slide 2
About AXI
2
AMBA AXI is a parallel communication protocol
multi master
multi slave
High performance
High Frequency
Used (also) inside the processors.
Notes: Course name
Lesson name
© 2000 - Author's name
2

## Slide 3
What it does
3
Read
Write
Two ways to communicate:
AXI has the role to enable such connections
Notes: Course name
Lesson name
© 2000 - Author's name
3

## Slide 4
How does it do it
4
Address mapping
Handshake protocol:
For each line (address, data and BRESP); valid ready resp
Notes: Course name
Lesson name
© 2000 - Author's name
4

## Slide 5
How it’s made
5
https://www.allaboutcircuits.com
Notes: Course name
Lesson name
© 2000 - Author's name
5

## Slide 6
Let’s break the magic
6
How to connect
Master to Slave
Slave to Master
DEMUX
MUX
The MUX and DEMUX need to be driven in some way… How? Let’s go on
Notes: Course name
Lesson name
© 2000 - Author's name
6

## Slide 7
The helm
7
To who belongs this address to?
DECODER
When is the address valid? When does the connecction end?
FSM
Notes: Course name
Lesson name
© 2000 - Author's name
7

## Slide 8
FSM States
8
RESET
IDLE
ERR STATE
ADDR HS
RESP HS
DATA HS
Notes: Course name
Lesson name
© 2000 - Author's name
8

## Slide 9
The Final Recepit
9
Finally, to build our AXI we used:
1) Big MUXs and DEMUXs
2) Sequential Circuits (decoder’s mapper)
3) FLIP FLOPS (to keep the signal of decoder)
4) FSM
5)Lot of patience 6) Love q.b.
Notes: Course name
Lesson name
© 2000 - Author's name
9

## Slide 10
On the AXI
10
ADDR HS
DATA HS
RESP HS
IDLE
ERR STATE
Standard Case:
Handshake on Address
Handshake on Data
Handshake on Response
Error Case:
Error on the Decoder
Switching to DE/MUX states
Completing the transaction with resp = 111
Notes: Course name
Lesson name
© 2000 - Author's name
10

## Slide 11
Difference Between AXI(s)
11
Features of AXI:
Burst transaction (AxLEN, AxBURST, xLAST)
Different width of the data bus (AxSIZE)
Different type of accesses (AxLOCK, AxCACHE)
Multi-size registers can be implemented (xSTRB)
Support Out of Order transactions
Support Quality of Service
Features of AXI-Lite:
Burst length = 1
Always use full width of the data bus
All accesses are Normal, Non-modifiable, Non-bufferable
Multi-size registers can be implemented
Need In Order transactions
Do not support Quality of Service
Notes: Course name
Lesson name
© 2000 - Author's name
11

## Slide 12: Before connection: protocol adaptation
Simple wire connection for the signals used by both AXI3 and AXI4-lite
Control signals of AXI3 without particular specification, for example:
  AxLEN = 0  no burst lenght
  AxSIZE = 2  data of 32 bit
  AxLOCK = 1  normal access mode
  AxUSER = 0  no usage
Not significant control on RREADY and BREADY

## Slide 13: Before connection: mapping addresses
Not only on the decoder but also on the address map

## Slide 14: After connection: RREADY and BREADY
RREADY and BREADY always asserted  can’t be used by read and write finite state machine!

## Slide 15: After connection: Write handshake
Slave can answer for both address and data at the same time  AXI can’t stay behind!

## Slide 16: Compare Uart decoding
ARM Design Start
Our AXI