## Slide 1: Embedded Systems Project : AXI4-lite Prof. W. Fornaciari Prof. D. Zoni Tutor: Andrea Galimberti
Group
Colombi Marco
Corbetta Giorgio
Consonni Cesare

## Slide 2
About AXI
2
AMBA AXI is a parallel communication protocol
multi master
multi slave
High performance
High Frequency
Used (also) inside the processors.
Notes: Course name
Lesson name
© 2000 - Author's name
2

## Slide 3
What it does
3
Read
Write
Two ways to communicate:
AXI has the role to enable such connections
Notes: Course name
Lesson name
© 2000 - Author's name
3

## Slide 4
How does it do it
4
Address mapping
Handshake protocol:
For each line (address, data and BRESP); valid ready resp
Notes: Course name
Lesson name
© 2000 - Author's name
4

## Slide 5
How it’s made
5
https://www.allaboutcircuits.com
Notes: Course name
Lesson name
© 2000 - Author's name
5

## Slide 6
Difference Between AXI(s)
6
Features of AXI:
Burst transaction (AxLEN, AxBURST, xLAST)
Different width of the data bus (AxSIZE)
Different type of accesses (AxLOCK, AxCACHE)
Multi-size registers can be implemented (xSTRB)
Support Out of Order transactions
Support Quality of Service
Features of AXI-Lite:
Burst length = 1
Always use full width of the data bus
All accesses are Normal, Non-modifiable, Non-bufferable
Multi-size registers can be implemented
Need In Order transactions
Do not support Quality of Service
Notes: Course name
Lesson name
© 2000 - Author's name
6

## Slide 7
Let’s break the magic
7
How to connect
Master to Slave
Slave to Master
DEMUX
MUX
The MUX and DEMUX need to be driven in some way… How? Let’s go on
Notes: Course name
Lesson name
© 2000 - Author's name
7

## Slide 8
The helm
8
Who belongs this address to?
DECODER
When is the address valid? When does the connecction end?
FSM
Notes: Course name
Lesson name
© 2000 - Author's name
8

## Slide 9
FSM States
9
RESET
IDLE
ERR STATE
ADDR HS
RESP HS
DATA HS
Notes: Course name
Lesson name
© 2000 - Author's name
9

## Slide 10
On the AXI
10
ADDR HS
DATA HS
RESP HS
IDLE
ERR STATE
Standard Case:
Handshake on Address
Handshake on Data
Handshake on Response
Error Case:
Error on the Decoder
Switching to DE/MUX states
Completing the transaction with resp = 111
Notes: Course name
Lesson name
© 2000 - Author's name
10

## Slide 11
The Final Recepit
11
Finally, to build our AXI we used:
1) Big MUXs and DEMUXs
2) Sequential Circuits (decoder’s mapper)
3) FLIP FLOPS (to keep the signal of decoder)
4) FSM
5)Lot of patience 6) Love q.b.
Notes: Course name
Lesson name
© 2000 - Author's name
11

## Slide 12: Before connection: protocol adaptation
Simple wire connection for the signals used by both AXI3 and AXI4-lite
Control signals of AXI3 without particular specification, for example:
  AxLEN = 0  no burst lenght
  AxSIZE = 2  data of 32 bit
  AxLOCK = 1  normal access mode
  AxUSER = 0  no usage
Not significant control on RREADY and BREADY

## Slide 13: Before connection: mapping addresses
Not only on the decoder but also on the address map

## Slide 14: After connection: RREADY and BREADY
RREADY and BREADY always asserted  can’t be used by read and write finite state machine!

## Slide 15: After connection: Write handshake
Slave can answer for both address and data at the same time  AXI can’t stay behind!

## Slide 16: Uart decoding
In reverse order with start and end bit
buffer

## Slide 17
How we tested it?
17
How the AXI is:
What we shuld have done:
Create fake Memory and stub our AXI
We managed to fit our AXI right inside the processor with no other changes
BUT
With an adapter, we put our AXI into the M3, and the simulations had only original or our AXI as differences
Notes: Course name
Lesson name
© 2000 - Author's name
17

## Slide 18: Compare Uart decoding
ARM Design Start
Our AXI