## Slide 1
Embedded Systems Project : AXI4-lite Prof. W. Fornaciari Prof. D. Zoni Tutor: Andrea Galimberti
Group
Colombi Marco
Corbetta Giorgio
Consonni Cesare

## Slide 2
About AXI
<number>
AMBA AXI is a parallel communication protocol
multi master
multi slave
High performance
High Frequency
Used (also) inside the processors.
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 3
What it does
<number>
Read
Write
Two ways to communicate:
AXI has the role to enable such connections
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 4
How does it do it
<number>
Address mapping
Handshake protocol:
For each line (address, data and BRESP); valid ready resp
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 5
How it’s made
<number>
https://www.allaboutcircuits.com
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 6
Let’s break the magic
<number>
How to connect
Master to Slave
Slave to Master
DEMUX
MUX
The MUX and DEMUX need to be driven in some way… How? Let’s go on
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 7
The helm
<number>
To who belongs this address to?
DECODER
When is the address valid? When does the connecction end?
FSM
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 8
FSM States
<number>
RESET
IDLE
ERR STATE
ADDR HS
RESP HS
DATA HS
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 9
The Final Recepit
<number>
Finally, to build our AXI we used:
1) Big MUXs and DEMUXs
2) Sequential Circuits (decoder’s mapper)
3) FLIP FLOPS (to keep the signal of decoder)
4) FSM
5)Lot of patience 6) Love q.b.
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 10
On the AXI
<number>
ADDR HS
DATA HS
RESP HS
IDLE
ERR STATE
Standard Case:
Handshake on Address
Handshake on Data
Handshake on Response
Error Case:
Error on the Decoder
Switching to DE/MUX states
Completing the transaction with resp = 111
Notes: Course name
Lesson name
© 2000 - Author's name
<number>

## Slide 11
Difference Between AXI(s)
<number>
Features of AXI:
Burst transaction (AxLEN, AxBURST, xLAST)
Different width of the data bus (AxSIZE)
Different type of accesses (AxLOCK, AxCACHE)
Multi-size registers can be implemented (xSTRB)
Support Out of Order transactions
Support Quality of Service
Features of AXI-Lite:
Burst length = 1
Always use full width of the data bus
All accesses are Normal, Non-modifiable, Non-bufferable
Multi-size registers can be implemented
Need In Order transactions
Do not support Quality of Service
Notes: Course name
Lesson name
© 2000 - Author's name
<number>